## Slide 1
FUSION ENGINEERING · THERMAL ANALYSIS
ITER Divertor Thermal Simulation
A 1D transient heat-conduction model: analytical solution, finite-difference simulation, and validation
q'' = 20 MW/m² plasma heat flux
k = 170–340 W/m·K tungsten conductivity

## Slide 2
01 · PROBLEM & MOTIVATION
Why divertor heat management matters
What is a divertor? The divertor is the component at the bottom of a tokamak that removes plasma exhaust and impurities, absorbing the most intense heat loads of the entire reactor. Why it's critical It faces steady-state heat fluxes of 10–20 MW/m² — comparable to a spacecraft re-entering the atmosphere. Without effective cooling, surface temperatures would exceed the melting point of any known structural material.
10–20 MW/m²
plasma heat flux at divertor surface
~3400°C
tungsten melting point — the operating margin
1D model
our simplified engineering approximation
1

## Slide 3
02 · PHYSICAL MODEL
Simplified 1D divertor geometry
PLASMA
q'' = 2×10⁷ W/m²
Divertor material (tungsten)
x = 0 (surface)
x = L (cooled)
L = 10 mm
COOLANT
T = 373 K (100°C)
Heat enters at the plasma-facing surface (x = 0) and is conducted through the material thickness L to a fixed-temperature cooling boundary at x = L. The problem is treated as one-dimensional: temperature varies only through the thickness, not along the surface.
2

## Slide 4
03 · ASSUMPTIONS
Simplifications behind the model
1
Homogeneous material
Uniform composition throughout the divertor block — no grain structure, coatings, or defects.
2
1D heat conduction
Temperature depends only on depth x; lateral (in-plane) conduction is neglected.
3
Constant k, ρ, cₚ
Thermal conductivity, density, and specific heat do not vary with temperature.
4
Fixed cooling boundary
The coolant-side face is held at a constant T_cool = 373 K at all times.
3

## Slide 5
04 · GOVERNING EQUATION
The 1D heat-conduction PDE
ρcₚ ∂T/∂t = k ∂²T/∂x²
ρ density (kg/m³)
cₚ specific heat capacity (J/kg·K)
k thermal conductivity (W/m·K)
T(x,t) temperature field
This is the transient heat equation: the left side is the rate of thermal energy storage, the right side is the net conduction into a slice of material. Setting ∂T/∂t = 0 gives the steady-state limit used for our analytical solution.
4

## Slide 6
05 · BOUNDARY & INITIAL CONDITIONS
Closing the problem
Plasma heat-flux BC (x = 0)
T[0] = T[1] + q''·Δx / k
A fixed heat flux enters the surface; the surface temperature floats and is set from its neighbor and the flux.
Cooling BC (x = L)
T[-1] = T_cool = 373 K
The coolant-side face is clamped at a constant temperature for all time.
Initial condition
T(x, 0) = T_cool everywhere
The divertor starts uniformly at the coolant temperature before plasma heating begins.
5

## Slide 7
06 · ANALYTICAL SOLUTION
Closed-form steady-state profile
T(x) = T_cool + (q'' / k)(L − x)
Integrating the steady-state equation (∂²T/∂x² = 0) twice and applying the two boundary conditions gives a linear temperature profile — heat flows down a straight-line gradient from the hot surface to the cooled base.
961.2 K (688°C) predicted surface temperature at q'' = 20 MW/m², k = 340 W/m·K, L = 10 mm
Chart: Steady-State Profile
| 0.0 | 0.5 | 1.1 | 1.6 | 2.1 | 2.6 | 3.2 | 3.7 | 4.2 | 4.7 | 5.3 | 5.8 | 6.3 | 6.8 | 7.4 | 7.9 | 8.4 | 8.9 | 9.5 | 10.0
Temperature | 961.24 | 930.28 | 899.32 | 868.36 | 837.4 | 806.44 | 775.48 | 744.52 | 713.56 | 682.6 | 651.64 | 620.68 | 589.72 | 558.76 | 527.8 | 496.84 | 465.88 | 434.92 | 403.96 | 373
6

## Slide 8
07 · NUMERICAL METHOD
Discretization & finite-difference scheme
1. Discretize space & time
Divide the thickness L into N = 50 points spaced Δx apart, and step forward in time in increments of Δt.
2. Approximate the derivatives
Replace ∂T/∂t with a forward difference and ∂²T/∂x² with a central difference — the explicit FTCS scheme.
3. March forward in time
At each step, update every interior point, then reapply the two boundary conditions.
Finite-difference equation
Tᵢⁿ⁺¹ = Tᵢⁿ + α·Δt·(Tᵢ₊₁ⁿ − 2Tᵢⁿ + Tᵢ₋₁ⁿ) / Δx²
α = k / (ρcₚ) is the thermal diffusivity — how quickly heat spreads through the material.
α = 6.59×10⁻⁵ m²/s for tungsten in the transient case (k = 170 W/m·K)
7

## Slide 9
08 · NUMERICAL STABILITY
Keeping the explicit scheme well-behaved
r = α·Δt / Δx² ≤ 0.5
The explicit FTCS scheme is only conditionally stable. If r exceeds 0.5, numerical errors grow without bound and the simulation diverges — the time step must shrink as the grid is refined.
Our run
Δx
0.204 mm (N = 50)
Δt
1×10⁻⁴ s
α
6.59×10⁻⁵ m²/s
r
0.158 → stable ✓
8

## Slide 10
09 · TRANSIENT RESULTS
Temperature evolving with time
Chart: Depth profile at successive times
| 0.0 | 1.0 | 2.0 | 3.1 | 4.1 | 5.1 | 6.1 | 7.1 | 8.2 | 9.2
t = 0.0001 s | 385.0048 | 373 | 373 | 373 | 373 | 373 | 373 | 373 | 373 | 373
t = 0.01 s | 432.8979 | 389.0935 | 375.4929 | 373.2059 | 373.0086 | 373.0002 | 373 | 373 | 373 | 373
t = 0.05 s | 499.4964 | 447.0114 | 412.1922 | 391.6095 | 380.8608 | 375.9345 | 373.9629 | 373.2765 | 373.0691 | 373.0141
t = 0.2 s | 619.9668 | 563.7359 | 516.8297 | 478.7386 | 448.6466 | 425.5091 | 408.1414 | 395.3001 | 385.744 | 378.2677
t = 10.0 s | 961.2353 | 901.2113 | 841.1872 | 781.1632 | 721.1392 | 661.1152 | 601.0912 | 541.0672 | 481.0432 | 421.0192
385 K → 961 K surface temperature rises from the initial coolant temperature to steady state within seconds. The profile straightens into the linear analytical shape as t → steady state, confirming the transient solution relaxes to the correct limit.
9

## Slide 11
10 · PARAMETER STUDY
Sensitivity of surface temperature
Heat flux (MW/m²)
Chart: 
| 5 | 10 | 15 | 20 | 25
Heat flux (MW/m²) | 520.06 | 667.12 | 814.18 | 961.24 | 1108.29
Conductivity k (W/m·K)
Chart: 
| 50 | 100 | 150 | 200 | 250 | 300
Conductivity k (W/m·K) | 4373 | 2373 | 1706.33 | 1373 | 1173 | 1039.67
Thickness (mm)
Chart: 
| 2 | 4 | 6 | 8 | 10 | 12
Thickness (mm) | 490.65 | 608.29 | 725.94 | 843.59 | 961.24 | 1078.88
Surface temperature rises linearly with heat flux and thickness, and falls off with conductivity — exactly as the analytical formula T = T_cool + q''L/k predicts.
10

## Slide 12
11 · VALIDATION
Numerical vs analytical solution
Chart: Steady-state comparison
| 0.0 | 0.6 | 1.2 | 1.8 | 2.4 | 3.1 | 3.7 | 4.3 | 4.9 | 5.5 | 6.1 | 6.7 | 7.3 | 8.0 | 8.6 | 9.2 | 9.8
Numerical | 961.2353 | 925.2209 | 889.2065 | 853.192 | 817.1776 | 781.1632 | 745.1488 | 709.1344 | 673.12 | 637.1056 | 601.0912 | 565.0768 | 529.0624 | 493.048 | 457.0336 | 421.0192 | 385.0048
Analytical | 961.2353 | 925.2209 | 889.2065 | 853.1921 | 817.1777 | 781.1633 | 745.1489 | 709.1345 | 673.12 | 637.1056 | 601.0912 | 565.0768 | 529.0624 | 493.048 | 457.0336 | 421.0192 | 385.0048
The two curves overlap almost exactly — the explicit finite-difference simulation, once it reaches steady state, reproduces the closed-form linear solution to within a fraction of a degree.
11

## Slide 13
12 · ERROR ANALYSIS
How closely the methods agree
2.92e-5 K
Maximum error
1.86e-5 K
Mean error
3.04e-6 %
Max relative error
Errors of this size are essentially numerical round-off, not modeling error — the finite-difference scheme is highly accurate once it has relaxed to steady state, well below any physically meaningful temperature difference.
12

## Slide 14
13 · GRID CONVERGENCE
Does the answer depend on grid size?
Chart: Surface temperature vs grid size
| N=25 | N=50 | N=100 | N=200
Surface T (K) | 961.2353 | 961.2353 | 961.2353 | 961.2353
Grid × time-step pairs (r = 0.4)
N Surface T (K) Error (K)
25 961.2353 2.00e-5
50 961.2353 2.91e-5
100 961.2353 3.48e-5
200 961.2353 3.80e-5
All grids converge to the same ~961.2 K surface temperature — the solution is grid-independent, so N = 50 is an adequate resolution for this problem.
13

## Slide 15
14 · PHYSICAL INTERPRETATION
What the results mean
Linear gradient
A constant-property, constant-flux slab always produces a straight-line temperature profile — curvature would only appear with temperature-dependent properties or internal heat generation.
Fast thermal response
With α ≈ 6.6×10⁻⁵ m²/s and only 10 mm of material, the divertor reaches steady state in well under a second — much faster than typical plasma pulse durations.
Conductivity is the lever
Because ΔT = q''L/k, doubling conductivity halves the surface temperature rise — this is why tungsten (high k) is favored over lower-conductivity armor materials.
Thin walls run cooler
Reducing thickness L reduces the temperature rise proportionally, motivating thin, actively-cooled divertor tile designs.
14

## Slide 16
15 · LIMITATIONS & FUTURE WORK
Where the model could go next
1D model — ignores lateral spreading and edge effects present in real, finite tiles.
Constant material properties — real k, ρ, cₚ vary with temperature, especially over an 600 K rise.
Idealized cooling — a perfectly fixed boundary temperature ignores real coolant-channel heat-transfer limits.
Possible extensions
→ 2D/3D geometry with realistic tile shapes
→ Temperature-dependent k, ρ, cₚ
→ Convective boundary condition (finite heat-transfer coefficient)
→ Pulsed/transient plasma heat-flux loading
15